| Water Services Department Monaghan County Council |  |
| --- | --- |

Details and information required by the Water Services Department to be submitted when applying for Planning Permission for the following:-

- Outline planning application for single housing or non-domestic unit, extensions or change of use, proposing to connect to a public water supply, public wastewater system or public storm water.

- Full planning application for single housing or non-domestic unit, extensions or change of use, proposing to connect to a public water supply, public wastewater system   or public storm water.

- Outline or Full planning application for All multiple housing units, Commercial premises, Non-domestic developments or Mixed use developments proposing to connect to a public water supply, public wastewater system   or public storm water.

Planning Information Notice

This information notice applies to all types of planning applications.

The  planning  authority  is  obliged  to  make  a  decision  on  a  valid  planning  application within  8  weeks  of  receiving  it, unless  it  needs  further  information from the applicant.  In order to allow  for  the  full  and  reasoned  assessment  of  a  variety of types of planning applications, from a Water  Services  perspective, in relation to water supply  system, storm water system, foul sewerage  system  and  associated  connections, the   following  information  is  deemed  to  be  essential  for  submission  with  application.  In  absence  of  relevant  information  this  could  delay  the application  by  up  to  4  weeks  or  longer, therefore  it  is  in  the  interest  of  the  applicant  to  ensure  that  a  comprehensive, fully  documented  application  is  submitted  at  the  outset.

It should be noted that this information and detail is not a pre-requisite for validation of the planning application under the provisions of the Planning Regulations 2001, however its absence may result in a delay in the determination of the application due to a further request for this information.

*Please Note

- Please note 6 copies of all information to be submitted with planning applications

- This list may not cover all items required to be submitted. Please consult Water Services Department Technical Guidance Document for further technical specification and requirements on proposals for water supply, and foul and storm sewers detail.

- Each application will be assessed through the planning process.

- It  should  be  noted  that  further  details  and  information  may  be  required  on  a  site  specific  basis.

- Additional information may be requested as detailed by the technical staff of the Water Services Department on receipt of any application.

1. Information to be submitted with Outline planning application for:-

Single housing or non-domestic unit, extensions or change of use, proposing to connect to a public water supply, public wastewater system   or public storm water.

- Contour survey of site: Indicate levels to Ordnance Survey (Malin Head Bench Mark) datum at 500mm increments.

- Site layout Plan to Scale 1:500 showing water supply proposals, foul sewerage proposals and storm water proposals. Details to indicate roads and buildings. Location of proposed connection to existing public mains / group scheme / sewer system / watercourse.

- Location of any existing public / private services traversing the site to be clearly shown on site layout plan including distances marked from proposed development.  Any wayleaves or right of ways to be clearly shown as per planning regulations.

- Letter  of  consent  and  associated  maps  giving  agreement  for  construction  and  use  of   pipelines serving the development, which will traverse private property other than that of the applicant (relevant  to  water  supply, storm  sewer  and  foul  sewer). The applicant is responsible for ensuring that all wayleaves are obtained and registered in the applicants favour.

- Letter of consent from group scheme Secretary for connecting to Group Water / Sewerage Scheme as appropriate.

#### The following information may be required to be submitted on a site specific basis:

- Location of all existing watermains, foul sewers, storm sewers and connection/service pipelines to be clearly shown on site layout plan and to include, pipeline material and diameter, invert levels, cover levels, existing and proposed ground levels, direction of flow, location of manholes, valves, hydrants, bulk meters, etc.  Colour coding of foul, storm and water system to be used to ensure clarity.

- Longitudinal sections  to  an  approved  scale  of  all  proposed  foul and storm services and  connection  to  existing  collection system.  Indicate pipe diameter and types, invert levels and cover  levels  of  manholes, 	location of manholes, existing & proposed ground levels, gradients & chainages, bedding  and  surround details (relevant  to  foul  sewers and storm  sewers).

- Flood risk assessment may be required in certain circumstances.

2. Information to be submitted with Full planning application for:

Single housing or non-domestic unit, extensions or change of use, proposing to connect to a public water supply, public wastewater system   or public storm water

- Contour survey of site: Indicate levels to Ordnance Survey (Malin Head Bench Mark) datum at 500mm increments.

- Site layout Plan to Scale 1:500 showing water supply proposals, foul sewerage proposals and storm water proposals. Details to indicate roads and buildings. Location of proposed connection to existing public mains / group scheme / sewer system / watercourse.

- Location of all existing watermains, foul sewers, storm sewers and connection/service pipelines to be clearly shown on site layout plan and to include, pipeline material and diameter, invert levels, cover levels, existing and proposed ground levels, direction of flow, location of manholes, valves, hydrants, bulk meters, etc.  Colour coding of foul, storm and water system to be used to ensure clarity.

- Location of any existing public / private services traversing the site to be clearly shown on site layout plan including distances marked from proposed development.  Any wayleaves or right of ways to be clearly shown as per planning regulations.

- Longitudinal sections  to  an  approved  scale  of  all  proposed  foul and storm services and  connection  to  existing  collection system.  Indicate pipe diameter and types, invert levels and cover  levels  of  manholes, 	location of manholes, existing & proposed ground levels, gradients & chainages, bedding  and  surround details (relevant  to  foul  sewers and storm  sewers).

- Letter  of  consent  and  associated  maps  giving  agreement  for  construction  and  use  of   pipelines serving the development, which will traverse private property other than that of the applicant (relevant  to  water  supply, storm  sewer  and  foul  sewer). The applicant is responsible for ensuring that all wayleaves are obtained and registered in the applicants favour.

- Flood risk assessment may be required in certain circumstances.

- Letter of consent from group scheme Secretary for connecting to Group Water / Sewerage Scheme as appropriate.

3. Information  to  be  submitted  with  Outline  or  Full  planning  application  for:-

All multiple housing units, Commercial premises, Non-domestic developments or Mixed use developments proposing to connect to a public water supply, public wastewater system   or public storm water.

Water Supply, Foul Sewer and Storm Sewer

- Contour survey of site. Indicate levels to Ordnance Survey (Malin Head bench mark) datum at 500mm increments.

- Separate Site layout Plan to Scale 1:500 detailing water supply in proposed development.  Indicate all roads and building. Location of existing and proposed mains water supply pipeline and service connections to be shown including pipe diameter and material. Location of all  hydrants, air  valves, sluice valves, scour  valves, meters and individual  connections  to  each  dwelling, location of proposed connection to existing public mains/group water scheme to be indicated.

- Separate Site layout Plan to Scale 1:500, detailing proposed Foul sewer system. Indicate all roads and buildings. Location of all existing foul sewers, storm sewers and connection/service pipelines to be clearly shown on site layout plan and to include, pipeline material and diameter, gradient, invert levels, cover levels, existing and proposed ground levels, direction of flow, location of manholes, etc. Location of proposed connection to existing public sewer/private sewer is to be clearly shown.  Colour coding of existing and proposed foul water system to be used to ensure clarity.

- Separate Site layout Plan to Scale 1:500, detailing proposed Storm water sewer system.  Details to include all existing open and underground drains, on or adjacent to the site and proposed location for final disposal. Location of all existing storm sewers and connection/service pipelines to be clearly shown on site layout plan and to include, pipeline material and diameter, gradient, invert levels, cover levels, existing and proposed ground levels, direction of flow, location of manholes, etc.  Colour coding of existing, proposed, foul and storm water system to be used to ensure clarity.

- Location of any existing public / private services traversing the site to be clearly shown on site layout plan including distances marked from proposed development.  Any wayleaves or right of ways to be clearly shown as per planning regulations. A separate layout plan maybe required to ensure clarity of information.

- Separate Longitudinal sections  to  an  approved  scale  for each of  all  proposed water supply pipelines, foul sewers and storm sewers and  connection  to  existing  services   indicating:- pipe  material and diameter, invert  level  and  cover  levels  of  manholes, location  of  manholes  and  valves, existing & proposed ground levels, gradients & chainages, bedding  and  surround  details.  (Relevant to foul sewers, storm sewers and watermains). For clarification proposes individual sectional details shall be provided for foul sewer, storm sewer and water supply.

- Total  volume of foul  waste  which  will  be generated by the development  detailing  peak foul flows (litres/sec)

- Total  volume of storm run  off  which  will  be generated by the development  detailing  peak  storm  flows (litres/sec)

- Detailed hydraulic analysis of the development  for both storm  sewer & foul collection and  disposal system  providing  verification  that  the  gradients and pipe sizes will produce flow velocities lying  in  the  range  between  0.75m/sec  and  3.0m/sec  in  the  main  sewer  pipelines.

- Detailed hydraulic design calculations demonstrating the capacity of the existing watercourse/public storm sewer/private storm sewer to receive and cater for the additional design storm flows and runoff from the proposed development.

- Flood risk assessment may be required in certain circumstances.

- Construction details for: manhole construction including drop manhole, bedding & surround of pipelines,   hydrants, sluice valves, air valves, scour valves and meter chambers.

- Letter of consent  from  group  scheme  Secretary  for  connecting to Group Water/Sewerage Scheme as  appropriate

- Letter of consent to provide legally binding wayleaves and right of ways, if required, and associated  maps  for  construction  and  use  of  pipelines,   serving  the  development, which  will  traverse private property other than that of the applicant (relevant  to  water  supply, storm  sewer  and  foul  sewer). The applicant is responsible for ensuring that all wayleaves are obtained and registered in the applicants favour.

Storm Attenuation

It is the policy of Monaghan County Council to limit storm run off from any new or proposed developments to a rate compatible with the existing site storm run-off presently discharging to the existing watercourse/storm sewer, and provide approved attenuation and flow control on site.

- Hydraulic design  of  storm  run  off  to  be  attenuated  to  be  calculated  on  the  basis  of  a  1  in  30  year  storm  return  period or other such return period deemed necessary by Monaghan County Council

- Proposals to be submitted of design details, structural drawings and proposals for construction of an  attenuation  storage system  capable  of  retaining  the  additional  storm  run  off  which  will  be  generated  from  the  proposed  development.

- Structural  drawings  and  proposals  for  provision/construction  of  “Hydrobrake”™, or equal approved  flow  control  device  on  storm  water  discharge  from  the  development  prior  to  discharge  to  existing  drain/watercourse.

- Longitudinal section is required through the proposed attenuation storage tank clearly indicating design and all  invert  and  cover  levels  of  storage system,  invert  level  of  inlet  and outlet pipelines  to and from the  system,  invert  level  of  discharge  pipeline downstream of attenuation  system,  invert  level  of  existing  watercourse  at  discharge  location,  maximum  top  water  level  of  watercourse  at  discharge  location,  existing  and  proposed  ground  levels to be clearly shown.

- Location  of  proposed  attenuation  tank/system  and  “Hydrobrake”™, or equal approved, facility  to  be  clearly  indicated  on  a 1/500  scale, site  layout  plan.

Oil Interceptor/ Separators

Where Oil interceptors are proposed within the development the following information is to be submitted

- Location of all proposed oil interceptors to be clearly indicated in the storm sewer site layout plan.

- Technical design and structural details to be submitted, showing the type / class of interceptor to be installed. The interceptor shall be capable of handling the flows equivalent to, or greater than, the maximum storm run-off possible from the development.

Please refer to Water Services Department Technical Staff for further technical specification and requirements on proposals for oil separators/ interceptors and storm attenuation systems in relation to storm sewers.

Pumping Stations

If the applicant is proposing to include a pumping station in the development the following information is required.

- Structural drawings and details for pumping station indicating cover levels, invert levels and structural dimensions. Separate valve chamber external to pumping station to be indicated.

- Design calculation and performance charts for proposed pumps.

- Proposals for alarm warning system incorporating auto dial out facility.

- Proposals for maintenance agreement for pump station, electrical equipment and pumps.

- Structural  drawings  and  design detail of foul  sewer  overflow  holding tank  and  all  associated  pipelines (min  capacity 0.5m3 per house).

- Longitudinal section, plan and design calculations for proposed rising main.

- Details of  security fencing to pumping station  site, appropriate  to  the  surroundings, and details of proposals  for  vehicular  access  to  site.

- Detailed  layout  plan  to  scale  1:100  indicating  all  structures, levels, pipelines, valves, flow meter, kiosk,  fencing  and  vehicular  access  to  site.

- Details of decompression chamber including location levels, size etc.

Waste Water Treatment Plant for all applications

In order to construct a new Wastewater Treatment Plant within County Monaghan full approval and consent must be obtained in writing from Monaghan County Council’s Water Services Department and Environment Department.

If it is proposed to construct a new wastewater treatment plant as part of a development then extensive consultations with the Water Services Department and the Environmental Department of Monaghan County Council is essential.

Each stage of design or consultation must be given approval by Monaghan County Council.

As part of the approval process for such a development, a site suitability assessment on the proposed location of the treatment plant site is required to be carried out by Monaghan County Council technical staff. This should be arranged and completed prior to any detailed design commencing on proposed plant.

Note: Joint Venture applications will be considered in certain locations.

The following is a brief outline of the basic information required to be submitted with such a development:

- Location map

- Contour survey of site

- Site layout plan

- Process description document

- Longitudinal  section through plant from inlet to outlet

- Plant layout

- Detailed structural drawings of each unit/building of the plant

- specification and design criteria

- details  of  treatment process

- proposals  for nutrient removal

- scaled  flow  diagram  through  treatment  units  and  process

- effluent discharge standards

- proposals  for  sampling facilities

- proposals  for  quality control

- proposals  for  operation and maintenance of  the  plant

- impact assessment of effluent discharge on the receiving waters

- maintenance proposals

### GENERAL

The proposed foul sewer and storm sewer drainage systems and water distribution systems to serve the development to be designed and constructed in accordance with the following:

  - the specifications and details as set out in Section 3 of Department of Environment  publication “Recommendations For Site Development Works For Housing Areas” dated November 1998

  - “Sewers for Adoption, 6th Edition” March 2006 published by WRc plc

  - “Water Services Department Technical Specification Document” prepared by Monaghan County Council

A meeting with the Water Services Department technical staff at the pre-planning stage is recommended for all multiple housing applications. Telephone no. (047) 30571 or (047) 30504